## Slide 1: Bio-Inspired Backbone Geometry for Enhanced 3D Force Estimation in Continuum Robots
Noah Jones, T.K. Morimoto
Idea: We propose a new approach for estimating multiple point forces using only proximal-mounted sensors and changes in the robot’s backbone geometry.
Improved Force Sensing: We propose that varying the robot's backbone geometry enables more accurate estimation of unknown external loads. Optimization: We use MDO to find an optimal backbone design by maximizing the conditioning of the force-to-wrench Jacobian across multiple loading scenarios.
Design Evaluation: We compare designs numerically using manipulability ellipsoids. Superior geometries maximize the shortest axis (minimum singular value), ensuring sensitivity in all directions.
Experimental Validation: We compare two-point-force estimation for a cylindrical and optimized design in hardware. For inter-force separations greater than 8 cm, the optimized design achieves median absolute errors of approximately 0.05 N, 1.0 mm, and 2.2°—corresponding to performance improvements of 74%, 67%, and 66% respectively over the cylindrical baseline.
Sensing Through Shape: We illustrate how a simple, bio-inspired artifact, whisker geometry, can be extended to more complex loading cases in surgical robotics. Optimization: We show how optimization can be used to find an optimal backbone design, capable of resolving multiple point-loads that conventional cylindrical backbones cannot due to inherent sensing degeneracies.
Hardware Testing: We develop a custom testing rig featuring multiple PID controlled tensioning winches and a two-arm gimbal, capable of applying 3 tendon tensions, and 2 point-forces in 3D.
Motivation: Knowledge of robot-tissue interaction forces during surgery can reduce patient injury and improve quality of surgeon’s force feedback.
Existing approaches:
  Body-Mounted Sensing: Bulky, hard to sterilize.
                Visual-Based Sensing: Limited space for camera integration, obstructed line-of-sight to full robot body, may require a second incision.
                Proximal-Mounted Sensing: Challenging to uniquely resolve multiple point forces (often not enough sensor information).
Problem
Results
Approach
Significance