## Slide 1: Bio-Inspired Backbone Geometry for Multi-Point 3D Force Estimation in Continuum Robots
Problem
Motivation: Knowledge of robot-tissue interaction forces during surgery can reduce patient injury and improve quality of surgeon’s force feedback.
Goal: Estimate the magnitudes and locations of multiple point forces.
Body-Mounted Sensing (FBGs, EM, Resistive flex):
Pros: Very accurate Cons: Hard to sterilize, bulky, hard to integrate [1].
Visual-Based Sensing (Endoscopic cameras, fiducial tracking) :
Pros: Can resolve multiple point forces with high accuracy [2][3], easy to sterilize.
    Cons: Requires direct line-of-sight of robot body, camera space constraints.
  Proximal-Mounted Sensing (force/torque sensors, Tendon tension sensors):
    Pros: Works in blind environments, easy to sterilize, easy to integrate [4]
    Cons: Current approaches cannot resolve magnitudes and locations of multiple point forces (ill-posed inverse).
Approach
Idea: We propose estimating multiple point forces using proximal sensors and variations in robot backbone geometry.
Inspiration: Sensory appendages in animals (whiskers, antennae) use non-circular cross-sections and mass asymmetry to mechanically amplify weak signals—like torsion—that would otherwise be masked by dominant bending modes [5]. These geometries help overcome the ill-posed nature of multi-force sensing in straight cylindrical designs [6][7].
Method: We develop an optimization framework to find backbone geometries that maximize multi-contact force estimation accuracy. The backbone is modeled as a series of elliptical cross-sections, with the major and minor radii of each segment as design variables. The objective is to find geometries with well-conditioned Jacobians—ensuring sensor noise is not amplified into large force estimation errors.
Results
Design Evaluation: We compare designs numerically and graphically using manipulability ellipsoids. Superior geometries maximize the shortest axis (minimum singular value), ensuring sensitivity in all directions.
Experimental Validation: For inter-force separations greater than 8 cm, the optimized design achieves median absolute errors of approximately 0.05 N, 1.0 mm, and 2.2°—corresponding to performance improvements of 74%, 67%, and 66% respectively over the cylindrical baseline. Performance gains diminish at smaller separations but remain measurable.
Significance
Sensing Through Shape: Just as natural selection has shaped animals' sensory appendages to optimize perception for their specific environments, we extend this principle to design tendon-driven surgical robots with geometries tailored to the complex loading conditions they encounter.
Optimization: We show how optimization can be used to find an optimal backbone design, capable of resolving multiple point-loads that conventional cylindrical backbones cannot due to inherent sensing degeneracies.
Hardware Testing: We develop a custom testing rig featuring multiple PID controlled tensioning winches and a two-arm gimbal, capable of applying 3 tendon tensions, and 2 point-forces in 3D.
Noah Jones, T.K. Morimoto

## Slide 2
References
1. Gao, Anzhu, et al. "Body contact estimation of continuum robots with tension-profile sensing of actuation fibers." IEEE Transactions on Robotics 40 (2024): 1492-1508.
2. Aloi, Vincent, et al. "Estimating forces along continuum robots." IEEE Robotics and Automation Letters 7.4 (2022): 8877-8884.
3. Ferguson, James M., D. Caleb Rucker, and Robert J. Webster. "Unified shape and external load state estimation for continuum robots." IEEE Transactions on Robotics 40 (2024): 1813-1827.
4. Sadati, SM Hadi, et al. "Stiffness imaging with a continuum appendage: Real-time shape and tip force estimation from base load readings." IEEE Robotics and Automation Letters 5.2 (2020): 2824-2831.
5. Mohren, T. L., et al. "Coriolis and centrifugal forces drive haltere deformations and influence spike timing." Journal of the Royal Society Interface 16.153 (2019): 20190035.
6. Starostin, E. L., V. G. A. Goss, and G. H. M. van der Heijden. "Whisker sensing by force and moment measurements at the whisker base." Soft Robotics 10.2 (2023): 326-335.
7. Huet, Lucie A., John W. Rudnicki, and Mitra JZ Hartmann. "Tactile sensing with whiskers of various shapes: Determining the three-dimensional location of object contact based on mechanical signals at the whisker base." Soft robotics 4.2 (2017): 88-102.